## Slide 1: Graph Laplacians and Stabilisation of Vehicle Formations (July 27, 2001)
J. Alex Fax, Richard M. Murray
Michael Högele
Paderborn, 1-8-2004

## Slide 2: -Content-
1. Introduction
2. Problem setup
3. The Laplacian Matrix of a Graph
4. Stabilisation of Vehicle Formations
Examples of Location of Laplacian Eigenvalues
Conclusion

## Slide 3: 1. Introduction
Setting: A flock of vehicles (e.g. satellites) has only passive sensing information among each other.
State: For the moment some results are known for leader-follower models, i.e. the sensing information graph is an acyclic tree.
Disadvantages:
-low disturbance rejection
-over-reliance on a single vehicle
-global information of the graph structure

## Slide 4
Idea: Allowing more interconnection topologies and trying to obtain local criteria for the relative formation stabilisation.

## Slide 5: 2. Problem setup
Consider N vehicles with identical dynamics and their N linear control problems:
xi‘ = A xi + B ui (1)
Absolute state mesurement yi of vehicle i: yi = C1 xi (2)
Sensing vector zij of the sensed vehicle j by vehicle i, where Ji c {1..N}\{i} is the set of sensed vehicles by vehicle i (nonempty!). zij = C2 (xi-xj) (3)

## Slide 6
Norming the #Ji signal vectors zij to a single signal vector zi:
zi = (zi1+..+zi#Ji)/#Ji (4)
Now define a linear control law
K(s): (yi,zi)  ui
by solving a linear equation:
vi‘ = F vi + G1 yi +G2 zi (5)
ui := H vi + J1 yi +J2 zi (6)
x1
X3
Z31
Z21
Z3
x2

## Slide 7
For a nxn-Matrix A define another matrix of shape Nn x Nn by N times repeating A along the diagonal.
A°:=diag(N,A)
Inserting the equations
(2)&(3) in (6) this in (1) and
(3) in (4) together with (2) in (5)
with x = (x1,..,xn), v = (v1,..,vn), n = dim(xi)
delivers the total system in two equations:
x‘ = A°x+(BJ1C1)°x+(BJ2C2)° Lx+(BH)°v (7)
v‘ = F°v+(G1C1)°x+(G2C2)° Lx (8)

## Slide 8
Or together as one combined system (9):
with L containing the relative sensing information of the Ji in following form:
Lii = 1
Lij = -1/#Ji , j in Ji
Lij = 0 , else
where
L(n):=(Lij*I(n))ij of shape nN x nN

## Slide 9: 3. The Laplacian Matrix of a Graph
A Graph G=(, ) consists of a set of vertices  and a set of arcs .
For each arc a=(v,w) v,w in  are called tail and head respectively.
The in-degree of a vertex v is the number of arcs with tail v.
Demanded Properties of G:
1. Uniqueness of each arc a=(v,w) in .
2. No loops (v,v) in .
3. The in-degree of all vertices is at least 1.

## Slide 10
The adjacency matrix A of Graph G is a matrix of shape #x# with:
Aij=1 ,arc (vj,vi) in 
Aij=0 , else
Define a Matrix D of shape # x# with
Dii = in-degree(vi)
Dij = 0 , else
Define the Laplacian Matrix L of Graph G by
L := I – D-1 A
The Eigenvalues of L are related to structural properties of G.

## Slide 11
Basic properties of L with respect to G:
1. 0 is always Eigenvalue of L with Eigenvector e1.
2. The spectrum of L lies within the Gershgorin disc of radius 1 in  centered in 1.
3. If G is M-periodic there exist M Eigenvalues on the boundary of latter disc with an angular spacing 2/M.
4. If G is aperiodic the Spectrum lies within the open disc around 1 with radius 1.

## Slide 12: 4. Stabilisation of Vehicle Formations
Theorem 1:
A local controller K(s) stabilizes the total system (9)
if and only if the control law K(s): (yi, zi)  zi simultaniously stabilizes the N systems
xi‘ = A xi +B ui
  yi = C1 xi (10)
  zi = i C2 xi
  for the Eigenvalues i of L.

## Slide 13
Idea of the proof:
By Schur transformation of L, substitution of x and and a simple matrix identity you can achieve an upper triangular system, so that the stability of the system depends of the diagonal systems where the Eigenvalues rule.

## Slide 14
The problem as information flow diagram for each xi:
B
Int
A
C1
i C2
G1
G2
Int
H
J1
J1
xi‘
xi
xi
zi
F
Vi‘
vi
ui
yi

## Slide 15
Here you can see that yi and zi together go into the vi and i.e. the ui.
A prudent controller design could now be to split the system into two isolated problems:
1. An inner feedback circle for yi in order to stabilize the total system and
2. An outer feedback circle for zi in order to obtain the formation stabilisation.
Assumptions for the remainder of the text:
1. C1=0 i.e. yi=0, which means that there exists only an outer feedback circle.
2. The system matrix A has no Eigenvalues on the open RHP in .

## Slide 16
So the simplified problem has following information flow:
B
Int
A
i C2
G2
Int
H
J1
xi‘
xi
xi
zi
F
Vi‘
vi
ui

## Slide 17
In control engineering the state space system as considered here will be transformed by the laplace operator, which means the you obtain a system of algebraic equations with analogous information flow diagrams.
Specificially the solving of a differential equation for an open loop system is equivalent to the multiplication of the input with a transfer function G, which is of following form for general linear systems of our case:
G(s) = C2 (sI–A)-1 B

## Slide 18
Theorem 2:
Is the open-loop transfer function
G(s) = C2 (s–A)-1 B a SISO-system,
i.e. ui, yi and G are have dim 1, and
the net encirclement of all -i-1 by the Nyquist plot K(i)G(i) for  in  for all nonzero Eigenvalues i of L is zero,
then K(s) stabilizes the relative formation dynamics.
Idea of the proof:
Application of the control engineering Nyquist stability criterion upon the N resulting systems in Theorem 1.

## Slide 19
Excursion:
One of various versions of the Nyquist criterion in control engineering holds for a system of following form:
The closed loop system is stable if the range of the imaginary axis by the controlled open-loop transfer function K(s)G(s) intersects the negative real axis right of –1.
K(s)
G(s)

## Slide 20
Nyquist criterion (applied version here):
The closed loop system is stable if the number of counter-clockwise encirclements of –1 by the range of the open-loop transfer function
i K(i)G(i) is equal to the number of RHP poles of G(s) for all nonzero i.
This is equivalent to the first version of the criterion if you know that the poles of G(s) are the Eigenvalues of A that were assumed to be zero earlier.

## Slide 21
Argumentation of the proof:
If now the N-1 Nyquist plots of i K(i)G(i) does not effect a CCW encirclement of –1
then equivalently the single Nyquist plot of K(i)G(i) doesn‘t effect this for all -i-1.

## Slide 22
If G(s) is a MIMO, that means a matrix of form m1x m2 rewrite the Eigenvalues of L in following form i = 1+ i.
Consider bounds M: |i|  M for all nonzero i.
If you close the loop you obtain as closed loop transfer function (shape: quadratic matrix)
C(s) = G(s)K(s)(I + K(s)G(s))-1
Theorem 3:
K(s) stabilizes the MIMO formation G(s) if
(C(i))<M-1 for all  in 
This seems to be clear according to a paper of Zhou and Doyle about robustness analysis.

## Slide 23: 5. Location of Laplacian Eigenvalues
How does formation structure affect on Eigenvalue placement?
1. Complete Graph
L =

## Slide 24
Here the Eigenvalues are 0 and N-1 times 1+1/(N-1) repeated.
2. Acyclic Graph
This is the leader-follower-scenario.
The only Eigenvalue is 1 N times repeated.
(not every vertice is tail of at least one arc, thus no 0 eigenvalue). It´s excluded in our case because of the nonzero in-degree.

## Slide 25
3.Two cyclic graph
Such a graph is undirected thus the Eigenvalues are all real.
Eigenvalues:

## Slide 26
4. Single directed cyclic graph
Here the Eigenvalues lie on the boundary of the Gershgorin disc around 1 with radius 1 at ej(i-1)/2

## Slide 27
Qualitatively and heuristic statement of the author:
Consider as two extremes:
1. the complete graph:
-almost all Eigenvalues in one single locus
-maximal mixing rate of information
4. the single directed cycle:
(remember acyclic l-f-graphs are excluded!)
-maximal dispersion of the Eigenvalues
-very low information mixing
We can „see“:
The eigenvalue placement seems to have
to do with the mixing rate of information.

## Slide 28
Heuristic arguments:
In the first case the influence of one single vehicle´s dynamics are quickly averaged out, because of the high connection.
In the second case the cycle induces periodic forcing that will never be averaged out.

## Slide 29
A word about linear controller design:
There are three commonly used control laws:
1.Proportional controller
K(s) = Kp
Output = Kp e,
2.Differential controller
K(s) = Kd s
Output = Kd de/dt
(quick reaction)
3.Integral controller
K(s) = Ki/s
Output = Ki
(memory effect)

## Slide 30
Example: 6-vehicle formation
G(s) = exp(-s T)/s2
Mixed PD-control law:
K(s) = Kp + Kd s
If we now add one sensing
vector z65 we can see
that the Eigenvalues
of tend more to the imaginary
axis and become more instable.

## Slide 31
The first graph has two 3-cycles and two 2-cycles.
The reason for this loss of stability seems to lie in the fact that a new 3 cycle is created.

## Slide 32: 6.Conclusion
The complete graph would be optimal for the formation stabilisation.
But if the graph is not complete, the rule
„The more sensing the better it is.“ is wrong!
There is no rule given in the paper what formation is optimal, but it seems to be positive to avoid cycles wherever possible.
This is not the ultimate answer for the graph design but you have a stability criterion in order to check if a given sensing graph together with a given control law is stable.

## Slide 33
Thank you.